## Slide 1
Introduction to Networks v7.0 (ITN)
Module 10: Basic Router Configuration

## Slide 2: Module Objectives
Module Title: Basic Router Configuration
Module Objective: Implement initial settings on a router and end devices.
Topic Title | Topic Objective
Configure Initial Router Settings | Configure initial settings on an IOS Cisco router.
Configure Interfaces | Configure two active interfaces on a Cisco IOS router.
Configure the Default Gateway | Configure devices to use the default gateway.

## Slide 3: 10.1 Configure Initial Router Settings

## Slide 4: Basic Router Configuration Steps
Configure Initial Router Settings
Configure the device name.
Secure privileged EXEC mode.
Secure user EXEC mode.
Secure remote Telnet / SSH access.
Encrypt all plaintext passwords.
Provide legal notification and
save the configuration.
Router(config)# hostname hostname
Router(config)# enable secret password
Router(config)# line console 0 Router(config-line)# password password Router(config-line)# login
Router(config)# line vty 0 4 Router(config-line)# password password Router(config-line)# login
Router(config-line)# transport input {ssh | telnet}
Router(config)# service password encryption
Router(config)# banner motd # message #
Router(config)# end
Router# copy running-config startup-config

## Slide 5: Configure Initial Router Settings Basic Router Configuration Example
Commands for basic router configuration on R1.
Configuration is saved to
NVRAM.
R1(config)# hostname R1 R1(config)# enable secret class R1(config)# line console 0 R1(config-line)# password cisco R1(config-line)# login R1(config-line)# line vty 0 4 R1(config-line)# password cisco R1(config-line)# login
R1(config-line)# transport input ssh telnet
R1(config-line)# exit
R1(config)# service password encryption
R1(config)# banner motd #
Enter TEXT message. End with a new line and the #
*********************************************** WARNING: Unauthorized access is prohibited!
**********************************************
R1(config)# exit
R1# copy running-config startup-config

## Slide 6: Packet Tracer – Configure Initial Router Settings
Configure Initial Router Settings
In this Packet Tracer, you will do the following:
Verify the default router configuration.
Configure and verify the initial router configuration.
Save the running configuration file.

## Slide 7: 10.2 Configure Interfaces

## Slide 8: Configure Router Interfaces
Configure Interfaces
Configuring a router interface includes issuing the following commands:
Router(config)# interface type-and-number Router(config-if)# description description-text Router(config-if)# ip address ipv4-address subnet-mask
Router(config-if)# ipv6 address ipv6-address/prefix-length
Router(config-if)# no shutdown
It is a good practice to use the description command to add information about the network connected to the interface.
The no shutdown command activates the interface.

## Slide 9: Configure Router Interfaces Example
Configure Interfaces
The commands to configure interface G0/0/0 on R1 are shown here:
R1(config)# interface gigabitEthernet 0/0/0
R1(config-if)# description Link to LAN
R1(config-if)# ip address 192.168.10.1 255.255.255.0 R1(config-if)# ipv6 address 2001:db8:acad:10::1/64 R1(config-if)# no shutdown
R1(config-if)# exit
R1(config)#
*Aug 1 01:43:53.435: %LINK-3-UPDOWN: Interface GigabitEthernet0/0/0, changed state to down
*Aug 1 01:43:56.447: %LINK-3-UPDOWN: Interface GigabitEthernet0/0/0, changed state to up
*Aug 1 01:43:57.447: %LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/0/0, changed state to up

## Slide 10: Configure Router Interfaces Example (Cont.)
Configure Interfaces
The commands to configure interface G0/0/1 on R1 are shown here:
R1(config)# interface gigabitEthernet 0/0/1
R1(config-if)# description Link to R2
R1(config-if)# ip address 209.165.200.225 255.255.255.252 R1(config-if)# ipv6 address 2001:db8:feed:224::1/64 R1(config-if)# no shutdown
R1(config-if)# exit
R1(config)#
*Aug 1 01:46:29.170: %LINK-3-UPDOWN: Interface GigabitEthernet0/0/1, changed state to down
*Aug 1 01:46:32.171: %LINK-3-UPDOWN: Interface GigabitEthernet0/0/1, changed state to up
*Aug 1 01:46:33.171: %LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/0/1, changed state to up

## Slide 11: Verify Interface Configuration
Configure Interfaces
To verify interface configuration use the show ip interface brief and
show ipv6 interface brief commands shown here:
R1# show ip interface brief
IP-Address 192.168.10.1
OK? Method Status YES manual up
209.165.200.225 YES manual up
Protocol up
up
Interface GigabitEthernet0/0/0 GigabitEthernet0/0/1 Vlan1
unassigned YES unset administratively down down
R1# show ipv6 interface brief
GigabitEthernet0/0/0 [up/up] FE80::201:C9FF:FE89:4501 2001:DB8:ACAD:10::1
GigabitEthernet0/0/1 [up/up] FE80::201:C9FF:FE89:4502 2001:DB8:FEED:224::1
Vlan1 [administratively down/down]
unassigned
R1#

## Slide 12: Configure Verification Commands
Configure Interfaces
The table summarizes show commands used to verify interface configuration.
Commands | Description
show ip interface brief show ipv6 interface brief | Displays all interfaces, their IP addresses, and their current status.
show ip route show ipv6 route | Displays the contents of the IP routing tables stored in RAM.
show interfaces | Displays statistics for all interfaces on the device. Only displays the IPv4 addressing information.
show ip interfaces | Displays the IPv4 statistics for all interfaces on a router.
show ipv6 interfaces | Displays the IPv6 statistics for all interfaces on a router.

## Slide 13: Configure Verification Commands (Cont.)
Configure Interfaces
View status of all interfaces with the show ip interface brief and show ipv6 interface
brief commands, shown here:
R1# show ip interface brief
IP-Address 192.168.10.1
OK? Method Status YES manual up
209.165.200.225 YES manual up
Protocol up
up
unassigned YES unset administratively down down
Interface GigabitEthernet0/0/0 GigabitEthernet0/0/1 Vlan1
R1#
R1# show ipv6 interface brief
GigabitEthernet0/0/0 [up/up] FE80::201:C9FF:FE89:4501 2001:DB8:ACAD:10::1
GigabitEthernet0/0/1 [up/up] FE80::201:C9FF:FE89:4502 2001:DB8:FEED:224::1
Vlan1 [administratively down/down] unassigned
R1#

## Slide 14: Configure Verification Commands (Cont.)
14
© 2016 Cisco and/or its affiliates. All rights r
eserved. Cisco Confidential
Configure Interfaces
Display the contents of the IP routing tables with the show ip route and show ipv6
route commands as shown here:
R1# show ip route
< output omitted>
Gateway of last resort is not set
192.168.10.0/24 is variably subnetted, 2 subnets, 2 masks
C 192.168.10.0/24 is directly connected, GigabitEthernet0/0/0 L 192.168.10.1/32 is directly connected, GigabitEthernet0/0/0
209.165.200.0/24 is variably subnetted, 2 subnets, 2 masks
C 209.165.200.224/30 is directly connected, GigabitEthernet0/0/1 L 209.165.200.225/32 is directly connected, GigabitEthernet0/0/1 R1#
R1# show ipv6 route
<output omitted>
C 2001:DB8:ACAD:10::/64 [0/0]
via GigabitEthernet0/0/0, directly connected L 2001:DB8:ACAD:10::1/128 [0/0]
via GigabitEthernet0/0/0, receive C 2001:DB8:FEED:224::/64 [0/0]
via GigabitEthernet0/0/1, directly connected
L 2001:DB8:FEED:224::1/128 [0/0]
via GigabitEthernet0/0/1, receive L FF00::/8 [0/0]
via Null0, receive
R1#

## Slide 15: Configure Verification Commands (Cont.)
Configure Interfaces
Display statistics for all interfaces with the show interfaces command, as shown here:
a0e0.af0d.e140)
R1# show interfaces gig0/0/0
GigabitEthernet0/0/0 is up, line protocol is up
Hardware is ISR4321-2x1GE, address is a0e0.af0d.e140 (bia
Description: Link to LAN
Internet address is 192.168.10.1/24
MTU 1500 bytes, BW 100000 Kbit/sec, DLY 100 usec, reliability 255/255, txload 1/255, rxload 1/255
Encapsulation ARPA, loopback not set Keepalive not supported
Full Duplex, 100Mbps, link type is auto, media type is RJ45
output flow-control is off, input flow-control is off
ARP type: ARPA, ARP Timeout 04:00:00
Last input 00:00:01, output 00:00:35, output hang never Last clearing of "show interface" counters never
drops: 0
Input queue: 0/375/0/0 (size/max/drops/flushes); Total output Queueing strategy: fifo
Output queue: 0/40 (size/max)
5 minute input rate 0 bits/sec, 0 packets/sec
5 minute output rate 0 bits/sec, 0 packets/sec 1180 packets input, 109486 bytes, 0 no buffer Received 84 broadcasts (0 IP multicasts)
0 runts, 0 giants, 0 throttles
<output omitted>
R1#

## Slide 16: Configure Verification Commands (Cont.)
Configure Interfaces
Display IPv4 statistics for router interfaces with the show ip interface command, as shown here:
R1# show ip interface g0/0/0
GigabitEthernet0/0/0 is up, line protocol is up Internet address is 192.168.10.1/24 Broadcast address is 255.255.255.255
Address determined by setup command MTU is 1500 bytes
Helper address is not set
Directed broadcast forwarding is disabled Outgoing Common access list is not set Outgoing access list is not set
Inbound Common access list is not set Inbound access list is not set Proxy ARP is enabled
Local Proxy ARP is disabled Security level is default Split horizon is enabled
ICMP redirects are always sent ICMP unreachables are always sent ICMP mask replies are never sent IP fast switching is enabled
IP Flow switching is disabled
<output omitted>
R1#

## Slide 17: Configure Verification Commands (Cont.)
Configure Interfaces
Display IPv6 statistics for router interfaces with the show ipv6 interface command shown here:
R1# show ipv6 interface g0/0/0
GigabitEthernet0/0/0 is up, line protocol is up
IPv6 is enabled, link-local address is
FE80::868A:8DFF:FE44:49B0
No Virtual link-local address(es): Description: Link to LAN
Global unicast address(es):
2001:DB8:ACAD:10::1, subnet is 2001:DB8:ACAD:10::/64
Joined group address(es):
FF02::1 FF02::1:FF00:1 FF02::1:FF44:49B0
MTU is 1500 bytes
ICMP error messages limited to one every 100 milliseconds ICMP redirects are enabled
ICMP unreachables are sent
ND DAD is enabled, number of DAD attempts: 1
ND reachable time is 30000 milliseconds (using 30000) ND NS retransmit interval is 1000 milliseconds
R1#

## Slide 18: 10.3 Configure the Default Gateway

## Slide 19: Default Gateway on a Host
Configure the Default Gateway
The default gateway is used when a host sends a packet to a device on another network.
The default gateway address is generally the router interface address attached to the local network of the host.
To reach PC3, PC1 addresses a packet with the IPv4 address of PC3, but forwards the packet to its default gateway, the G0/0/0 interface of R1.
Note: The IP address of the host and the
router interface must be in the same network.

## Slide 20: Default Gateway on a Switch
Configure the Default Gateway
A switch must have a default gateway address configured to remotely manage the switch from another network.
To configure an IPv4 default gateway on a switch, use the ip default- gateway ip-address global configuration command.
MEDIA IS WORKING ON A CORRECTED VERSION OF THE GRAPHIC FROM 10.3.2.
IT IS WRONG ON AR, AND ON THE GLOBAL BUG LIST
STOP

## Slide 21: Packet Tracer – Connect a Router to a LAN
Configure Initial Router Settings
In this Packet Tracer, you will do the following:
Display the router information.
Configure router interfaces.
Verify the configuration.

## Slide 22: Packet Tracer – Troubleshoot Default Gateway Issues
Configure Initial Router Settings
In this Packet Tracer, you will do the following:
Verify the network documentation and use tests to isolate problems.
Determine an appropriate solution for a given problem.
Implement the solution.
Test to verify the problem is resolved.
Document the solution.

## Slide 23: 10.4 Module Practice and Quiz

## Slide 24: Packet Tracer – Basic Device Configuration
Configure Initial Router Settings
In this Packet Tracer, you will do the following:
Complete the network documentation.
Perform basic device configurations on a router and a switch.
Verify connectivity and troubleshoot any issues.

## Slide 25: Lab – Build a Switch and Router Network
In this Lab, you will complete the following objectives:
Set up the topology and initialize devices.
Configure devices and verify connectivity.
Display device information.
Configure Initial Router Settings

## Slide 26: What did I learn in this module?
Module Practice and Quiz
The tasks that should be completed when configuring initial settings on a router.
  Configure the device name.
  Secure privileged EXEC mode.
  Secure user EXEC mode.
  Secure remote Telnet / SSH access.
  Secure all passwords in the config file.
  Provide legal notification.
  Save the configuration.
For routers to be reachable, the router interfaces must be configured.
  Using the no shutdown command activates the interface. The interface must also be connected to another device, such as a switch or a router, for the physical layer to be active. There are several commands that can be used to verify interface configuration including the show ip interface brief and show ipv6 interface brief, the show ip route and show ipv6 route, as well as show interfaces, show ip interface and show ipv6 interface.

## Slide 27: What did I learn in this module (Cont.)?
Module Practice and Quiz
For an end device to reach other networks, a default gateway must be configured.
  The IP address of the host device and the router interface address must be in the same network.
A switch must have a default gateway address configured to remotely manage the
switch from another network.
  To configure an IPv4 default gateway on a switch, use the ip default-gateway ip- address global configuration command.